To install lock and carriage into the shroud.

- Sit the lock in the palm of one hand with the key toward you and the locking pin to your left.

- Push the carriage down onto the lock with the hook away from you, so that the locking pin of the padlock remains clear of the carriage. Ensure the lock is seated completely into the carriage.

- If not already unlocked, unlock the padlock and pull the lock shackle pin fully out.

- Ensure the doors are open so the staple/hasp is not protruding into the shroud body.

- Holding the carriage and lock vertically with the carriage hook at the top pointing away from you and the carriage back plate (not shown) towards you.  Push them up into the shroud about midway along until the carriage hook cannot go any further up.

- Keeping the lock and carriage vertical, slide the lock and carriage to the left, maintaining a slight upward pressure.

- Towards the left end of the shroud the carriage should be able to be pushed further upwards into the top left corner of the shroud.

- Once this has been done, whilst maintaining an upward pressure on the carriage and lock, carefully slide them to the right.  If an obstruction is met, move the carriage back and forwards until the carriage slides back along the length of the shroud.

- Let the carriage down and it should now rest within the shroud and be able to be slid left and right towards and away from the rear aperture through which the staple will protrude when the doors are closed.

To remove lock and carriage from shroud.

- Open the door so that the staple is not protruding through the rear aperture of the shroud.

- Unlock and open the padlock, ensuring that the shackle pin is pulled fully down and open.

- Grasp the shackle pin and slide the lock and carriage to the left as far as possible.

- When you encounter an obstacle gently push the lock and carriage upwards, maintaining pressure to the left.

- The carriage and lock should then move further to the left into the top left corner of the shroud.

- Without letting go, let the carriage and lock fall gently down and to the right until out of the shroud.

To move the carriage and lock from the parked position and lock the shroud to the staple.

- Close the doors, so that the staple is positioned protruding through the aperture in the rear of the shroud.

- Unlock the padlock and pull the shackle pin fully open.

- If the lock and carriage are in the ‘park’ position (i.e. right side of the shroud and cannot be slid across to the left), push the lock and carriage upwards, maintaining a pressure to the left.

- The carriage and lock should reach a point at which it is possible to continue sliding them to the left.

- Continue to slide the carriage and lock towards the staple (left-wards) until the open lock hits the staple.  There is ‘play’ in the carriage mechanism that allows you to move the lock around to align the lock with the staple, wherever it is in the rear aperture.

- Once aligned it should now be possible to push the shackle pin of the lock fully closed.  If it is catching on the staple, move the lock around slightly whilst still pushing upwards until it finds its way through the hole in the staple and push fully closed.

- Turn the key to lock padlock.

To unlock the lock and move it to the ‘Parked’ position.

- Reverse the procedure above to the point where you are sliding the lock back to the parked position.

- The carriage and lock should ride over a ramp to return to the parked position.  It might be necessary to assist with this by slightly lifting the carriage whilst sliding to the right.

- Once over the ramp the carriage will drop into the parked position and re-locked to secure it within the shroud body.

# Text boxes

Carriage and lock assembly

Shroud rear aperture

Shroud body outline

5

6

7

8

9

Carriage hook

Carriage and lock assembly

Shroud rear aperture

Shroud body outline

6

6

5

4

Carriage hook

Lock shackle pin

3

2

Shroud body outline

5

4

3

Carriage hook

Carriage and lock assembly

7

6

Lock shackle pin

Shroud rear aperture

Key

Staple